## Slide 1
DEVELOPER ESSENTIALS
Networking for Web Developers
Essential Networking Concepts Every Developer Should Know
Client → Server → Database → Response

## Slide 2
What We'll Cover
01
Network Fundamentals
What is a Network
Types of Networks
Network Devices
Router vs Switch
02
Core Concepts
IP & MAC Addresses
Default Gateway
DNS & ARP
NAT
03
Data Flow
LAN Communication
How a Website Loads
04
Web Protocols
HTTP vs HTTPS
Client-Server Architecture

## Slide 3
What is a Network?
A network is a collection of interconnected devices that can communicate and share resources with each other. Networks range from two devices to billions.
Real-Life Examples
WiFi
Wireless home and office networks
LAN
Wired local networks in schools and offices
Internet
Global network connecting billions of devices
Data Sharing
Devices exchange files, media, and resources
Core Purpose: Networks enable devices to exchange data efficiently and reliably, from simple file sharing to accessing global web services.
03

## Slide 4
Types of Networks
LAN
Local Area Network
Covers a small area like home, office, or school
Characteristics:
• High speed, low latency
• Privately managed
• Ethernet or WiFi
MAN
Metropolitan Area Network
Covers a city or large campus area
Characteristics:
• Bridges LAN and WAN
• ISP or municipality owned
• Fiber optic connections
WAN
Wide Area Network
Spans cities, countries, continents
Characteristics:
• The Internet is the largest WAN
• ISP-managed infrastructure
• Slower than LAN due to distance
Key Differentiator: Geographic scope and ownership model — LAN is private and local, WAN is global and ISP-managed, MAN sits in between.
04

## Slide 5
Network Devices
Router
Directs data between different networks using IP addresses. The "traffic director" of networking — decides the best path for data to travel.
Layer 3 (Network Layer)
Switch
Connects devices within the same network using MAC addresses. Enables efficient local communication by forwarding data only to the intended recipient.
Layer 2 (Data Link Layer)
Modem
Converts digital signals to analog (and vice versa) for transmission over ISP lines. Bridges your local network to the Internet.
Signal Conversion Device
Access Point
Creates a wireless (WiFi) connection point for devices to join a wired network. Extends network coverage without cables.
Wireless Bridge
05

## Slide 6
Router vs Switch
Router
Layer 3 — Network
Function
Connects different networks together
Addressing
Uses IP addresses for routing decisions
Scope
Inter-network communication
Analogy
Postal service between cities
Switch
Layer 2 — Data Link
Function
Connects devices within the same network
Addressing
Uses MAC addresses for forwarding
Scope
Intra-network communication
Analogy
Mail delivery within a neighborhood
Key Difference: Router handles traffic between networks | Switch handles traffic within a network
06

## Slide 7
IP Address
An IP (Internet Protocol) address is a unique numerical identifier assigned to every device on a network, enabling devices to find and communicate with each other.
IPv4
32-bit address
192.168.1.1
• Four octets (0-255) separated by dots
• ~4.3 billion unique addresses
• Most widely used today
IPv6
128-bit address
2001:0db8::1
• Eight groups of hex separated by colons
• 340 undecillion unique addresses
• Designed to replace IPv4
Public IP
Assigned by your ISP. Unique across the entire Internet. Identifies your network to the world.
Private IP
Assigned by router within local network. Reusable across private networks. Not reachable from the Internet.
07

## Slide 8
Private vs Public IP
Private IP Ranges (RFC 1918)
Class | Range | Use Case
Class A | 10.0.0.0 – 10.255.255.255 | Large enterprise networks
Class B | 172.16.0.0 – 172.31.255.255 | Medium-sized networks
Class C | 192.168.0.0 – 192.168.255.255 | Small home/office networks
Public IP
Globally unique address reachable from anywhere on the Internet
• Assigned by your ISP
• One per network (typically)
• Required for Internet access
Router's Role
The router assigns private IPs via DHCP and manages the single public IP from ISP
• NAT translates between them
• ~18M devices reuse same ranges
• Isolates local from global traffic
08

## Slide 9
MAC Address
MAC (Media Access Control) address is a hardware-level identifier burned into every Network Interface Card (NIC). It serves as a permanent, unique identity for each network device.
Address Format
00:1A:2B:3C:4D:5E
• 48-bit hexadecimal address
• 6 pairs of hex digits separated by colons
• First 3 pairs = manufacturer (OUI)
Key Properties
Unique
No two NICs share the same MAC address worldwide
Permanent
Burned into hardware at manufacturing time
Layer 2
Used for local network communication only
Every device with a network connection — laptop, phone, smart TV — has a unique MAC address
09

## Slide 10
IP vs MAC Address
Property | IP Address | MAC Address
Type | Logical (software-assigned) | Physical (hardware-burnt)
Can Change | Yes — dynamic via DHCP | No — permanent (mostly)
Scope | Works across networks (Layer 3) | Local network only (Layer 2)
Format | 192.168.1.1 (IPv4) | 00:1A:2B:3C:4D:5E
Purpose | Location-based routing | Device-specific identification
Both are essential: IP finds the destination network; MAC finds the destination device within that network. They work together at different layers.
10

## Slide 11
Default Gateway
The default gateway is the "exit door" of your local network — the device (typically a router) that routes traffic from your local devices to external networks, including the Internet.
Laptop
192.168.1.2
Phone
192.168.1.3
Smart TV
192.168.1.4
DEFAULT GATEWAY
(Router)
192.168.1.1
INTERNET
External Networks
Local Area Network (LAN)
Traffic flows through the Gateway to reach the Internet
Key Point: Without a default gateway, devices can only communicate within their own local subnet.
11

## Slide 12
DNS (Domain Name System)
DNS translates human-readable domain names (e.g., google.com) into machine-readable IP addresses (e.g., 142.250.80.46). It works like the "phonebook of the Internet."
Example Lookup
google.com
DNS Lookup
142.250.80.46
Why DNS is Needed
• Humans remember names, computers need numbers
• DNS lookups complete in under 100ms
• Without DNS, you'd memorize IP addresses
• Enables flexible server migration
Resolution Process
1. Browser checks cache
2. Queries DNS resolver
3. Asks root → TLD → authoritative server
4. IP address returned to browser
DNS is one of the most critical systems on the Internet — every web request starts with a DNS lookup
12

## Slide 13
ARP (Address Resolution Protocol)
ARP resolves IP addresses to MAC addresses within a local network. It bridges Layer 3 (IP) and Layer 2 (MAC) communication.
How ARP Works
1
ARP Request
Device broadcasts to all devices on the network:
"Who has this IP? Tell me your MAC!"
2
ARP Reply
The device with the matching IP responds directly:
"I have that IP. Here's my MAC!"
3
Cache & Communicate
Result is cached in the ARP table. Devices can now communicate directly using MAC addresses.
ARP Table Example
IP Address | MAC Address
192.168.1.2 | 00:1A:2B:3C:4D:5E
192.168.1.3 | 00:1A:2B:3C:4D:5F
192.168.1.4 | 00:1A:2B:3C:4D:60
Important: ARP only works within a local network (subnet). To reach devices outside the local network, traffic is sent to the default gateway first.
13

## Slide 14
NAT (Network Address Translation)
NAT translates multiple private IP addresses into a single public IP address, enabling entire networks to share one Internet connection.
How NAT Works
PRIVATE NETWORK
Laptop
192.168.1.2
Phone
192.168.1.3
Tablet
192.168.1.4
Smart TV
192.168.1.5
Printer
192.168.1.6
ROUTER
+ NAT
Translates
private → public
INTERNET
203.0.113.1
Single public IP from ISP
shared by all devices
NAT Types
Static NAT: One private IP maps to one public IP (1:1) | Dynamic NAT: Maps to a pool of public IPs | PAT (Port NAT): Many private IPs share one public IP using different ports — most common in homes
14

## Slide 15
How Devices Communicate in LAN
1
Check Destination
Device checks if destination IP is in the same subnet using subnet mask
2
ARP Request
If local, device sends ARP broadcast to find the destination MAC address
3
Create Frame
Builds Ethernet frame with source MAC and destination MAC addresses
4
Switch Forwards
Switch receives frame and forwards to correct port based on MAC table
5
Data Received
Destination device receives and processes the data
The Complete Flow
IP Check → ARP Resolution → Frame Creation → Switch Forwarding → Data Delivery
Note: If the destination IP is outside the local subnet, the device sends the frame to the default gateway (router) instead, which then routes it to the external network.
15

## Slide 16
How a Website Loads (Full Flow)
1
User Request
User types URL → Browser checks DNS cache → DNS lookup resolves domain to IP address
2
TCP Connection
Browser establishes TCP connection with server via 3-way handshake (SYN → SYN-ACK → ACK)
3
Network Routing
Request travels: Device → Router → NAT (private→public IP) → ISP → Internet backbone → Destination server
4
Server Response
Server processes request, queries database if needed, generates HTML/CSS/JS response, sends data back
5
Page Rendering
Browser receives response, parses HTML, fetches additional resources, renders DOM, applies CSS, executes JavaScript
16

## Slide 17
HTTP vs HTTPS
HTTP
Port 80
HyperText Transfer Protocol
• Data sent in plain text
• Vulnerable to interception
• No identity verification
• No data integrity checks
Unsecured — do not use for sensitive data
HTTPS
Port 443
HTTP Secure (HTTP + SSL/TLS)
• Data is encrypted end-to-end
• Server identity verified
• Data integrity protected
• Prevents MITM attacks
Standard for all modern websites
TLS provides three protections: Encryption (privacy) | Authentication (identity) | Integrity (no tampering)
17

## Slide 18
Client-Server Architecture
Client (Frontend)
User's browser or application
• Sends HTTP requests
• Renders UI/UX
• Handles user input
• Displays data to user
Request
Server (Backend)
Processes client requests
• Runs business logic
• Authenticates users
• Queries database
• Returns HTTP responses
Response
Database
Persistent storage
• Users
• Content
• Transactions
• Application data
Complete Request Flow
Client sends HTTP Request → Server processes + queries Database → Server builds Response → Client receives and renders
This three-tier architecture (Client → Server → Database) powers the vast majority of web applications
18

## Slide 19
KEY TAKEAWAYS
Understanding networking fundamentals makes you a better developer
Every line of code you write eventually travels across a network — knowing how that works gives you superpowers.
IP • MAC • DNS • ARP • NAT • HTTP/HTTPS • Client-Server